## Slide 1
Engineering summary
Recommended technology
Develop a variable-speed hygienic top-entry agitator with staged down-pumping axial-flow hydrofoils, hygienic baffles or validated off-center swirl control, and controlled closed…
Selection rationale
The controlling duty is not simple liquid blending. The system must rapidly draw down and dissolve 50–150 kg/m³ of powders that may float, raft, clump, or dissolve slowly while ma…
Selection criteria
Industry: Biopharmaceutical & Biologics; Host system: Media Preparation Vessel / hygienic solution preparation vessel; Validated DIR code: 3-3-3-3-3-2-3
Limitations
Anchor or frame agitator: Predominantly tangential, close-clearance flow is not the preferred primary mechanism for rapid powder drawdown and turbulent suspension in water-like me…
Media Preparation Vessel Mixing
Evaluation
Preliminary hygienic mixing comparison for high-load media preparation; SME review and representative testing remain required.
Validated DIR: 3-3-3-3-3-2-3
Project-team summary
Notes: Engineering summary from result fields:
Recommended technology: Develop a variable-speed hygienic top-entry agitator with staged down-pumping axial-flow hydrofoils, hygienic baffles or validated off-center swirl control, and controlled closed powder addition.
Selection rationale: The controlling duty is not simple liquid blending. The system must rapidly draw down and dissolve 50–150 kg/m³ of powders that may float, raft, clump, or dissolve slowly while maintaining low product shear and tightly limiting vortexing, air entrainment, and foam. A variable-speed top-entry agitator using one or more down-pumping axial-flow hydrofoils provides the strongest preliminary balance of high circulation per unit power, off-bottom sweeping, low localized shear, heat-transfer support, and scale-up familiarity. Multiple impellers are likely for the stated 1.5:1 to 2:1 liquid height-to-diameter ratio, but their number, diameter, spacing, and elevation require actual vessel geometry and vendor hydraulic analysis.
The expected base-fluid regime is turbulent for water-like media, although transient concentrated zones, cold operation, or polymeric ingredients could create locally viscous, non-Newtonian, or yield-stress behavior. Hydrofoil performance therefore needs confirmation using ingredient properties and representative powder-addition trials. The preliminary scale-up basis should preserve geometric similarity where practicable and evaluate power per volume, impeller tip speed, pumping capacity, blend time, and minimum suspension speed rather than relying on a single scale-up parameter. Published biopharmaceutical mixing work confirms that vessel geometry and hydrofoil arrangement materially affect mixing performance (Mixing in process vessels used in biopharmaceutical manufacturing, https://pubmed.ncbi.nlm.nih.gov/10753450/), while broader scale-up literature emphasizes characterization of hydrodynamics, fluid properties, and geometry (Development and Scale-Up of the Mixing Process, https://link.springer.com/chapter/10.1007/978-3-030-31415-6_22).
A hygienic top-entry arrangement introduces a rotating shaft penetration and associated seal boundary, but it offers better torque and suspension scalability for this volume and loading than a bottom-entry magnetic mixer. The seal arrangement must be developed for the numerical pressure/vacuum cycles, cleaning chemicals, allowable leakage, and contamination-control strategy. Product-contact surfaces, welds, internals, sanitary connections, drainability, spray coverage, and elastomer compatibility should be documented for qualification readiness. The DIR requires cleanability but does not establish aseptic service, SIP, or sterile operation; these must not be inferred. Risk- and science-based mixing qualification should demonstrate the ±2% endpoint at worst-case volume, temperature, ingredient sequence, powder loading, and permitted speed range (Risk- and Science-Based Media and Buffer Mixing Validations, https://ispe.org/pharmaceutical-engineering/march-april-2024/risk-and-science-based-media-and-buffer-mixing).
Selection criteria: Industry: Biopharmaceutical & Biologics; Host system: Media Preparation Vessel / hygienic solution preparation vessel; Validated DIR code: 3-3-3-3-3-2-3
Limitations: Anchor or frame agitator: Predominantly tangential, close-clearance flow is not the preferred primary mechanism for rapid powder drawdown and turbulent suspension in water-like media.; Helical-ribbon agitator: Intended mainly for laminar, very-high-viscosity service and adds unnecessary close-clearance internals for the expected media-preparation duty.; Recirculating jet-mixing system: Primary performance would depend on pump hydraulics and nozzle coverage, with increased concern for low-level coverage, dead zones, loop cleanability, and reliable powder suspension.

## Slide 2
Equipment assessment / Media Preparation Vessel
Design basis from DIR code
WORKING VOLUME
2,000–10,000 L
LIQUID GEOMETRY
H/D approximately 1.5:1–2:1
POWDER LOADING
50–150 kg/m³
UNIFORMITY TARGET
±2% within 15 minutes
OPERATING TEMPERATURE
2–80 °C
PROCESS BOUNDARY
Closed; pressure and full vacuum
Selection implication
Tall geometry and difficult powders favor staged, low-shear axial pumping with engineered swirl control. Final power, shaft, impellers, seal, and baffles require geometry, rheology, pressure, and tri…
Project-team summary • Slide 2
Basis: user DIR code 3-3-3-3-3-2-3

## Slide 3
Equipment assessment / Media Preparation Vessel
Mixing objectives, constraints and failure modes
1
Establish bulk circulation
Use staged axial pumping with every operating impeller submerged.
2
Incorporate powder
Feed closed and controlled above a qualified drawdown zone.
3
Dissolve difficult components
Maintain turnover and temperature without unqualified high-shear exposure.
4
Confirm concentration uniformity
Sample top, middle, bottom, wall, and outlet locations.
What can go wrong
• Rapid charging causes rafting, fish-eyes, and dissolution beyond 15 minutes.
• Vortexing entrains gas, generates foam, and compromises endpoint measurements.
• Settling creates nonuniform heels, outlet blockage, and restart overload.
• Low levels uncover impellers, increasing aeration and weakening heel mixing.
Target outcome
Demonstrate dissolution and ±2% uniformity within 15 minutes without unacceptable shear, foam, deposits, or cleaning residue.
Project-team summary • Slide 3
Basis: user DIR code 3-3-3-3-3-2-3

## Slide 4
Equipment assessment / Media Preparation Vessel
Realistic mixing-system options
Mixing type
Notes
Fit
Top-entry hydrofoil agitator
Best preliminary balance of axial pumping, suspension, low shear, and…
Best
Top-entry retreat-curve agitator
Cleanable multipurpose alternate; powder drawdown and endpoint requir…
Strong
Top-entry pitched-blade turbine
Robust suspension option; higher shear, power, foam, and aeration ris…
Strong
Recirculating inline rotor-stator
Optional closed powder wetting; localized shear and CIP burden requir…
Add-On
Bottom-entry magnetic agitator
Seal advantage; 10,000 L torque, turnover, solids, and restart remain…
Conditional
Recommendation: Advance staged top-entry hydrofoils as the preliminary basis; retain retreat-curve impellers as the cleanability-led alternate.
Project-team summary • Slide 4
Basis: user DIR code 3-3-3-3-3-2-3

## Slide 5
Equipment assessment / Media Preparation Vessel
Option evaluation matrix
Option
Technical
GMP
Scale-up
Cost
Reliability
Rank
Top-entry hydrofoil agitator
Best
High
Low-Medium
Strong
High
1
Top-entry retreat-curve agitator
Strong
High
Medium
Strong
High
2
Top-entry pitched-blade turbine
Strong
High
Medium
Best
High
3
Recirculating inline rotor-stator
Add-on
Medium-High
Medium-High
Conditional
Medium
4
Bottom-entry magnetic agitator
Conditional
High
High
Conditional
Medium-High
5
Decision logic Ranking prioritizes low-shear pumping, powder drawdown, tall-vessel turnover, hygienic integration, and scalable suspension. Results may change with rheology, minimum level, quantified shear limits,…
Project-team summary • Slide 5
Basis: user DIR code 3-3-3-3-3-2-3

## Slide 6
Equipment assessment / Media Preparation Vessel
Recommended basis and alternate option
Recommended selection
Preliminary basis: VFD-driven hygienic top-entry agitator with staged down-pumping hydrofoils and engineered…
• Efficient axial pumping supports turnover and suspension at comparative…
• Multiple stages address tall geometry, bottom sweeping, heat transfer,…
• Variable speed enables fill, addition, dissolution, hold, restart, and…
• Scale-up can evaluate pumping, power, tip speed, blend time, and suspen…
Alternate option
Alternate: Hygienic top-entry retreat-curve impeller arrangement with multiple stages where cleanab…
Retain subject to representative powder-drawdown and 15-minute endpoint trials; expected suspension…
Cons / watchouts
• Top shaft penetration requires seal development for pressure, v…
• Long shaft requires critical-speed, runout, support-load, and m…
• Powder performance remains sensitive to feed location, rate, le…
• Final impeller geometry and drive sizing await vessel, rheology…
Project-team summary • Slide 6
Basis: user DIR code 3-3-3-3-3-2-3

## Slide 7
Equipment assessment / Media Preparation Vessel
Preliminary specification points / vendors / references
Baseline specification
• Configuration — fixed 2,000–10,000 L 316L vessel; VFD top-entry drive;…
• Swirl control — drainable hygienic baffles or validated off-center arra…
• Seal — qualify actual pressure, full vacuum, 2–80 °C, cleaning chemistr…
• Controls — speed/load monitoring, level permissives, torque and seal al…
• Qualification start — submerge lowest stage; establish low-speed circul…
• Powder addition — use closed, controlled-rate charging; increase speed…
• Endpoint — test top, middle, bottom, near-wall, and outlet locations ag…
Manufacturer shortlist
• Top-entry hydrofoil — SPX FLOW Lightnin; EKATO; Philadelphi…
• Retreat-curve — Alfa Laval; ZETA; SPX FLOW; GMM Pfaudler
• Pitched-blade turbine — SPX FLOW Lightnin; EKATO; Philadelp…
• Inline wetting add-on — Silverson Flashmix; YSTRAL Conti-TD…
• Bottom magnetic alternate — Alfa Laval LeviMag; ZETA; Steri…
Do not specify
• Anchor or frame as primary — tangential flow poorly suits…
• Helical ribbon as primary — intended for sustained lamina…
• Recirculating jets as primary — coverage, dead zones, cle…
Project-team summary • Slide 7
Basis: user DIR code 3-3-3-3-3-2-3