## Slide 1
Engineering summary
Capacity / duty
400 L packed resin
Sizing basis
Screening required bed volume for 10 kg target protein per cycle at the conservative DIR lower-bound usable resin capacity of 25 mg/mL. Bec…
Envelope
Estimated installed equipment envelope: 2.2 m W × 2.2 m D × 3.0 m H. Packed bed basis: approximately 1.60 m internal diameter × 0.20 m bed…
Connections
Top process/mobile-phase inlet (quantity 1) 2 (DN50) in; Bottom process/product outlet and low-point drain (quantity 1) 2 (DN50) in; Top ve…
Open items / assumptions
REQUIRED: Confirmation that 10 kg is the target protein mass loaded per cycle rather than total batch mass.; REQUIRED: HIC binding mode and…
HIC Chromatography Column
Sizing
Initial screening of capacity, geometry, hydraulics, connections, pressure basis, envelope, and approval gaps.
Validated DIR: 2-3-3-2-3-1
Project-team summary
Notes: Engineering summary from result fields:
Capacity / duty: 400 L packed resin
Sizing basis: Screening required bed volume for 10 kg target protein per cycle at the conservative DIR lower-bound usable resin capacity of 25 mg/mL. Because the DIR capacity is explicitly a usable design capacity, no additional utilization factor was applied: 10,000,000 mg / 25 mg/mL = 400,000 mL = 400 L.
Envelope: Estimated installed equipment envelope: 2.2 m W × 2.2 m D × 3.0 m H. Packed bed basis: approximately 1.60 m internal diameter × 0.20 m bed height, providing 402 L. Recommended operating-space envelope: approximately 4.2 m W × 4.2 m D × 4.5 m H. m Generic cylindrical scale-up benchmarked against large-scale chromatography-column families. For 0.400 m3 packed resin and a selected 0.20 m bed height, ID = sqrt(4V/(pi H)) = 1.596 m, rounded to 1.60 m; resulting volume is 0.402 m3. Estimated installed width/depth add about 0.30 m per side for shell, frame, nozzles, valves, and instrument projections. Estimated height includes the 0.20 m bed plus approximately 2.8 m for plenums, distributors, end assemblies, support frame, adjustable top assembly/actuation, and connections. These allowances are estimates, not catalog dimensions.
Connections: Top process/mobile-phase inlet (quantity 1) 2 (DN50) in; Bottom process/product outlet and low-point drain (quantity 1) 2 (DN50) in; Top vent and air-displacement connection (quantity 1) 1 (DN25) in; Upper flush pressure-sensing connection (quantity 1) 1.5 (DN40) in; Lower flush pressure-sensing connection (quantity 1) 1.5 (DN40) in; Upper resin-slurry charging and packing connection (quantity 1) 3 (DN80) in; Lower resin-slurry discharge/unpacking connection (quantity 1) 3 (DN80) in; Outlet sample connection (quantity 1) 0.5 (DN15) in
Open items / assumptions: REQUIRED: Confirmation that 10 kg is the target protein mass loaded per cycle rather than total batch mass.; REQUIRED: HIC binding mode and whether product or impurity load controls capacity.; REQUIRED: Conditioned feed concentration and volume per cycle.; REQUIRED: Batch mass, cycles per batch, and acceptable batch processing window.; REQUIRED: Exact effective design capacity or condition-specific DBC with utilization factor.; REQUIRED: Exact loading residence time within >3 to 6 minutes.; REQUIRED: Complete step recipe and flow requirements.; REQUIRED: Peak and minimum flows for column-owned connection sizing.; REQUIRED: Sanitary connection standard, line-sizing criteria, and skid interface sizes.; SUPPLIER CONFIRMATION: Resin identity, particle size, rigidity/compressibility, swelling, packing method, allowable bed-height range, DBC test basis, pressure-flow curve, and cleaning limits.; COLUMN-VENDOR CONFIRMATION: Available column diameters, selected bed-volume capability, distributor turndown, pressure-rating definition, nozzle sizes, packing pressure, and physical envelope.; OPTIONAL REFINEMENT: Development-scale breakthrough curves, scale-up factors, fouling history, impurity loading, yield target, precipitation risk, resin lifetime, and re-use strategy.; SCREENING ASSUMPTION ALLOWED: Use f_util = 0.80 only if the available capacity is measured DBC rather than an already derated usable capacity.; SCREENING ASSUMPTION ALLOWED: Use water at 20 °C only as a noncontrolling reference case; concentrated salt and cleaning-fluid properties remain required for final hydraulic sizing.; SCREENING ASSUMPTION ALLOWED: Treat fluids as incompressible, Newtonian, and single phase only if precipitation and suspended solids are separately excluded.; The 10 kg value is target protein loaded per cycle, not total batch mass.; The target protein is the capacity-controlling binding species in a bind-elute HIC operation; impurity-binding or flow-through operation could require a different basis.; The DIR value of 25 to 50 mg/mL is treated as effective usable capacity, so the optional 0.80 DBC utilization factor is not applied.; One cycle is used for the per-cycle capacity calculation; cycles per batch do not reduce a requirement already specified per cycle.; A 30 cm packed-bed height is selected for screening because it is within the validated >25 to 40 cm range.; A 6 minute loading residence time is selected for screening. Final flow must use the process-selected residence time and the residence time associated with the confirmed DBC.; No additional resin-volume margin, packing allowance, scale-up allowance, or standard column-size rounding is included.; The governing process flow is based on the shortest DIR residence time: 400 L / 3 min = 133.3 L/min. The 6 min condition is 66.7 L/min.; For the 25-40 cm packed-bed-height range, 400 L corresponds to an approximate column internal diameter of 1.43 m at 25 cm bed height or 1.13 m at 40 cm bed height; final diameter and distributor design are vendor responsibilities.; The minimum pressure-boundary basis is 5 barg because the selected operating-pressure requirement extends to 5 bar. Design temperature, code test pressure, cyclic fatigue, and sanitary-clamp derating require vendor confirmation.; The column is not assumed to be vacuum rated. Venting is required during draining and cooling unless the vendor certifies full-vacuum capability.; All product-contact surfaces are assumed to be 316L stainless steel with hygienic finish suitable for biopharmaceutical chromatography; elastomers are assumed to be EPDM or PTFE subject to process-chemical compatibility review.; ASME BPE hygienic clamp ferrules are the selected end-connection convention. Equivalent vendor sanitary standards may be used only after dimensional, pressure-rating, and gasket compatibility confirmation.; The bottom 2 in process outlet is assumed to be the liquid low-point drain, so a separate small drain nozzle is not added.; Packed-bed integrity or HETP testing is performed through the normal process inlet and outlet; no dedicated integrity-test port is required.; No dedicated buffer nozzle is required because all load, buffer, wash, elution, regeneration, and CIP fluids enter through the common process inlet.; Slurry-port sizing assumes approximately 50 percent settled-resin fraction and a practical 200 L/min transfer rate. Final sizes depend on resin bead characteristics, slurry concentration, transfer hose length, and the column vendor's packing method.; A hydraulically or pneumatically actuated adjustable adapter was not specified. Any vendor-specific adapter-actuation connections must be identified and sized by the column vendor.

## Slide 2
Equipment assessment / HIC Chromatography
Validated design basis and key gaps
TARGET LOAD
10 kg/cycle sizing value
USABLE CAPACITY
>25–50 mg/mL usable
BED HEIGHT
>25–40 cm nominal
RESIDENCE TIME
>3–6 min loading
PRESSURE REQUIREMENT
>3–5 bar requirement
INSTALLATION BASIS
Reusable; in-place packing and cleaning
Selection implication
Sizing conservatively uses 25 mg/mL, 30 cm, 6 min, and 5 barg preliminary hardware rating. Confirm load interpretation, binding mode, exact DBC, recipe flows, fluid properties, and pressure-rating de…
Project-team summary • Slide 2
Basis: user DIR code 2-3-3-2-3-1

## Slide 3
Equipment assessment / HIC Chromatography
Sized-item concept and sizing criteria
1
Reusable column concept
Fixed sanitary column; pack, clean, and reuse in place.
2
Retain required capacity
Provide at least 400 L within DIR-compliant bed height.
3
Apply hygienic construction
Use drainable 316L geometry and ASME BPE clamp interfaces.
4
Meet pressure basis
Minimum 5 barg; no vacuum rating assumed.
What can go wrong
• Insufficient usable capacity or uncredited scale-up margin
• Excess bed pressure drop at high-salt viscosity
• Distributor maldistribution across the calculated 1.303 m diameter
• Vacuum damage during draining or cooling
Target outcome
Select a vendor configuration providing at least 400 L at a compliant bed height.
Project-team summary • Slide 3
Basis: user DIR code 2-3-3-2-3-1

## Slide 4
Equipment assessment / HIC Chromatography
Resin capacity, cycles, and selected bed volume
Mixing type
Notes
Fit
25 mg/mL endpoint
400 L gives 10 kg capacity; 0% credited margin.
Best
50 mg/mL endpoint
10 kg requires 200 L; not selection basis.
Conditional
Per-cycle basis
One cycle used; cycles per batch remain missing.
Strong
Utilization factor
Not applied because DIR states usable design capacity.
Limited
Selected bed volume
400 L calculated governing screen before vendor rounding.
Best
Selection basis: retain 400 L screening volume; confirm exact usable DBC and define positive design margin before freeze.
Project-team summary • Slide 4
Basis: user DIR code 2-3-3-2-3-1

## Slide 5
Equipment assessment / HIC Chromatography
Diameter, bed height, flow, velocity, and pressure checks
Option
Technical
GMP
Scale-up
Cost
Reliability
Rank
Bed geometry
400 L / 0.30 m =…
Calculated ID 1.3…
Distributor unifo…
Vendor rounding r…
Retain ≥400 L cap…
1
Selected loading
66.67 L/min at 6…
300 cm/h superfic…
Resin pressure-fl…
Recipe confirmati…
Within validated…
2
Flow boundary
133.33 L/min at 3…
Actual maximum mu…
Peak step flows m…
Skid interface un…
Connection screen…
3
Main nozzles
1.25 m/s through…
0.016 bar local l…
Bed and distribut…
Vendor hydraulic…
2 in DN50 prelimi…
4
Pressure boundary
5 barg preliminar…
0–6 barg instrume…
Rating definition…
Clamp derating re…
No vacuum rating…
5
Decision logic Geometry and nozzle checks support screening only; final acceptance requires resin pressure-flow data, controlling fluid properties, distributor losses, pump shutoff pressure, vendor MAWP, and compli…
Project-team summary • Slide 5
Basis: user DIR code 2-3-3-2-3-1

## Slide 6
Equipment assessment / HIC Chromatography
Column-owned connections and preliminary sizes
Recommended selection
Qty 1 each: 2 in DN50 top inlet; 2 in DN50 bottom outlet/drain; 1 in DN25 vent; two 1.5 in DN40 pressure port…
• 2 in inlet and outlet screen at 1.25 m/s.
• Bottom outlet serves true low-point liquid drainage.
• 1 in vent screens at 5.8 m/s displacement-air velocity.
• 3 in ports support estimated 800 L slurry transfer.
Alternate option
No dedicated utility nozzle, buffer nozzle, integrity port, or separate liquid drain.
Final packing-port arrangement may combine with vendor-standard slurry connections after drainabili…
Cons / watchouts
• Distributor, bed-support, valve, reducer, and external piping l…
• Vacuum capability, clamp derating, and final interfaces require…
• Sample connection is optional when downstream skid sampling is…
Project-team summary • Slide 6
Basis: user DIR code 2-3-3-2-3-1

## Slide 7
Equipment assessment / HIC Chromatography
Envelope, calculation summary, gaps, and actions
Baseline specification
• Selected geometry — Calculated: 400 L, 0.30 m bed, 1.3333 m² area, 1.30…
• Installed envelope — Estimate: 2.2 m W × 2.2 m D × 3.0 m H.
• Operating-space envelope — Estimate: 4.2 m W × 4.2 m D × 4.5 m H.
• Maintenance clearance — Estimate: 1.0 m around frame and 1.5 m overhead.
• Envelope benchmark used 1.60 m ID × 0.20 m bed and 402 L; rebase for se…
• Calculation summary — 10,000,000 mg / 25 mg/mL = 400 L; capacity margin…
• Flow summary — 66.67 L/min selected; 133.33 L/min three-minute boundary…
Manufacturer shortlist
• Repligen OPUS large-scale — Catalog benchmark only: 10–30 c…
• Cytiva BPG — Catalog benchmark only: up to 450 mm ID and 12…
• Commercial-scale or custom reusable-column vendor — Final m…
Do not specify
• Do not freeze the unrounded 1.3029 m diameter as a vendor…
• Do not use the 0.20 m benchmark bed as process geometry.
• Do not credit capacity above 25 mg/mL before DBC confirma…
• Do not claim packed-bed pressure drop without resin and f…
• Do not assume vacuum capability or catalog-model complian…
Project-team summary • Slide 7
Basis: user DIR code 2-3-3-2-3-1