## Slide 1
Chromatography Resin
Slurry Tank
Agitator and impeller recommendation for a 250–1,000 L stainless CIP/SIP slurry preparation tank.
Validated DIR: 3-1-2-2-3-2
Project-team summary
gentle
low-speed
bulk flow
Gentle suspension
for representative
column-packing slurry

## Slide 2
Agitator Selection / Chromatography Resin Slurry Tank
Design basis from DIR code
WORKING VOLUME
250–1,000 L
TANK FORMAT
Stainless fixed tank
SLURRY STRENGTH
20–50% settled resin
RESIN TOLERANCE
Moderately shear-sensitive
PRIMARY DUTY
Prepare slurry before column packing
CLEANABILITY
CIP/SIP stainless system
Selection implication
Avoid high local shear. Favor slow, bulk-circulation impellers that keep resin uniformly suspended and transfer-ready without bead attrition or air entrainment.
Project-team summary • Slide 2
Basis: user DIR code 3-1-2-2-3-2

## Slide 3
Agitator Selection / Chromatography Resin Slurry Tank
Mixing objectives and failure modes
1
Resin + buffer
Low-foam charge
2
Gentle resuspend
Lift settled bed
3
Homogenize / sample
Representative solids
4
Transfer to column
Stable slurry feed
What can go wrong
High-speed impellers can crack or abrade resin beads.
Dead zones create non-representative slurry concentration.
Air entrainment affects packing consistency and bed uniformity.
Hard-settled resin requires controlled resuspension, not aggressive shear.
Target outcome
A transfer-ready, homogeneous resin slurry produced with the lowest practical power input and validated by representative sampling.
Project-team summary • Slide 3
Basis: user DIR code 3-1-2-2-3-2

## Slide 4
Agitator Selection / Chromatography Resin Slurry Tank
Best-fit agitator shortlist
Agitator type
Resin protection
Suspension
CIP/SIP fit
Fit
Double-Helix Resin Agitator
Best
Low-Shear Axial Hydrofoil
Strong
Wide-Blade Pitched-Blade Turbine
Acceptable
Aseptic Magnetic Bottom Mixer
Conditional
Anchor/Sweep + Axial Kicker
Special case
Score key: five filled dots = strongest fit for this service.
Recommendation: select double-helix where available; use dual low-shear axial hydrofoils for custom stainless designs.
Project-team summary • Slide 4
Basis: user DIR code 3-1-2-2-3-2

## Slide 5
Agitator Selection / Chromatography Resin Slurry Tank
Recommended selection: Double-Helix Resin Agitator
Best technical fit
Dedicated resin slurry systems use slow, bulk-circulation motion to suspend resin gently and maintain a transfer-ready packing slurry.
low speed • high turnover • low shear
Preferred duty
Column-packing slurry preparation.
Moderately shear-sensitive agarose or polymeric resin.
20–50% settled resin volume at 250–1,000 L scale.
Closed stainless system with CIP/SIP validation.
Pros
Strong resin-protection profile.
Good top-to-bottom turnover at low speed.
Directly aligned with resin mixer package systems.
Cons / watchouts
More specialized than commodity impellers.
Supplier-specific vessel integration.
Requires recipe validation for speed, time and sample uniformity.
Project-team summary • Slide 5
Basis: user DIR code 3-1-2-2-3-2

## Slide 6
Agitator Selection / Chromatography Resin Slurry Tank
Alternative agitators and when to use them
Low-Shear Axial Hydrofoil
Use when: Custom stainless tank where a generic sanitary agitator is preferred.
Pros: Efficient axial flow; good suspension with lower shear than pitched blades.
Watchout: May need dual impellers and careful baffle design.
Wide-Blade PBT
Use when: Robust resin or difficult initial resuspension.
Pros: Proven solids suspension; readily sourced.
Watchout: Higher shear and power than hydrofoil.
Magnetic Bottom Mixer
Use when: Aseptic containment or low-heel recovery is the dominant driver.
Pros: No shaft seal; strong CIP/SIP advantages.
Watchout: May struggle with settled resin bed at 250–1,000 L.
Anchor/Sweep + Axial Kicker
Use when: High-solids or compacting resin bed with dead-zone risk.
Pros: Gentle bottom/wall sweeping.
Watchout: Complex, harder to clean and usually special-case.
Do not specify high-speed dispersers, rotor-stators, Rushton turbines, or aggressive recirculation loops for this resin duty.
Project-team summary • Slide 6
Basis: user DIR code 3-1-2-2-3-2

## Slide 7
Agitator Selection / Chromatography Resin Slurry Tank
Procurement-ready specification points
Baseline specification
Top-entry VFD-controlled agitator sized for 250–1,000 L working volume.
Impeller: double-helix resin agitator preferred; dual low-shear axial hydrofoils acceptable backup.
Low-speed recipe: resuspend → homogenize → sample → transfer.
Sanitary shaft/seal design, full CIP spray coverage and drainability.
Representative slurry sampling point and low-shear transfer pump.
Manufacturer shortlist
Cytiva — BioProcess Resin Mixer / dedicated resin slurry package.
AK Bio / Fluid Management — SLURIPREP slurry handling systems.
SPX FLOW Lightnin — sanitary mixers and A310/A510 hydrofoils.
Alfa Laval — hygienic agitators and LeviMag UltraPure.
ZETA / Steridose / Metenova — aseptic magnetic agitators.
EKATO / Jongia — custom hygienic agitator systems.
Decision: proceed with double-helix as basis of design; retain low-shear hydrofoil as second-source/custom-tank alternate.
References: Cytiva BioProcess Resin Mixer; Alfa Laval LeviMag UltraPure; SPX FLOW Lightnin A310/A510 hydrofoil; ZETA magnetic agitators; Lisure hygienic slurry tank.
Project-team summary • Slide 7
Basis: user DIR code 3-1-2-2-3-2